## Slide 1: eBPF Tools
Jules Irenge, Student, University of Manchester, LFX Mentee
Elana Copperman, PhD, Mobileye/Intel, LFX Mentor (ELISA)

## Slide 2: Agenda
Introduction to BPF
  Overview
  Applications and Issues
eBPF
  Overview
  How does it work
  What can eBPF do ?
  How to use BPF?
    bcc, bpftrace
    XDP (eXpress Data Path)
Support for safety
Demo tools

## Slide 3: Introduction

## Slide 4: OVERVIEW
Two Components:
  Network tap
  Packets filter

## Slide 5: Extended BPF
struct bpf_insn prog[] = {
BPF_MOV64_REG(BPF_REG_6, BPF_REG_1),
BPF_LD_ABS(BPF_B, ETH_HLEN + offsetof(struct iphdr, protocol) /* R0 = ip->proto */),
BPF_STX_MEM(BPF_W, BPF_REG_10, BPF_REG_0, -4), /* *(u32 *)(fp - 4) = r0 */
BPF_MOV64_REG(BPF_REG_2, BPF_REG_10),
BPF_ALU64_IMM(BPF_ADD, BPF_REG_2, -4), /* r2 = fp - 4 */
BPF_LD_MAP_FD(BPF_REG_1, map_fd),
BPF_RAW_INSN(BPF_JMP | BPF_CALL, 0, 0, 0, BPF_FUNC_map_lookup_elem),
BPF_JMP_IMM(BPF_JEQ, BPF_REG_0, 0, 2),
BPF_MOV64_IMM(BPF_REG_1, 1), /* r1 = 1 */
BPF_RAW_INSN(BPF_STX | BPF_XADD | BPF_DW, BPF_REG_0, BPF_REG_1, 0, 0), /* xadd r0 += r1*/
BPF_MOV64_IMM(BPF_REG_0, 0), /* r0 = 0 */
BPF_EXIT_INSN(),
};
eBPF or Just BPF
10x64-bit registers
maps(hashes)
Actions
Packets, kernel functions, user functions, tracepoint, user markers, PMCs
Alexei Starovoitov, 2014+

## Slide 6: eBPF
Run custom code in the kernel
Event-driven
Run when the kernel or an application passes a certain hook point.
Predefined hooks include system calls, function entry/exit, kernel tracepoints, network events, etc.
http://ebpf.io/what-is-ebpf

## Slide 7: What eBPF can do
Observability
  Tracing, debugging
  Tool: bcc, bpftrace
Networking
  SDN configuration,
  DDoS mitigation, Load balancing...
  Tool: XDP
Security
  Intrusion detection
  Tool: XDP
Safety – Network, kernel tracing

## Slide 8: How does eBPF/BPF work ?

## Slide 9: BPF runtime internals

## Slide 10: bpf() syscall

## Slide 11: BPF maps
key/values pair can store data of any kind for sharing between kernel and userspace
accessed from user space via BPF syscall
  Create a map map_fd = bpf(BPF_MAP_CREATE, union bpf_attr *attr, u32 size)
  Lookup key in a given map
  Create or update key/value pair
  Find and delete element in key/value pair in a given map
  Delete map
different types: hash, array, bloom filter, radix-tree, etc.

## Slide 12: eBPF Verifier
Determine the safety of the ebpf program, reject or accept ebpf bytecode.
  Does Directed acyclic Graph checks
    disallow unbounded loops and perform other CFG validations checks.
      detect instructions in the program that are unreachable
  Starts from instruction and check all possible paths
    simulates and observe state change of registers and stack

## Slide 13: Raw BPF
struct bpf_insn prog[] = {
BPF_MOV64_REG(BPF_REG_6, BPF_REG_1),
BPF_LD_ABS(BPF_B, ETH_HLEN + offsetof(struct iphdr, protocol) /* R0 = ip->proto */),
BPF_STX_MEM(BPF_W, BPF_REG_10, BPF_REG_0, -4), /* *(u32 *)(fp - 4) = r0 */
BPF_MOV64_REG(BPF_REG_2, BPF_REG_10),
BPF_ALU64_IMM(BPF_ADD, BPF_REG_2, -4), /* r2 = fp - 4 */
BPF_LD_MAP_FD(BPF_REG_1, map_fd),
BPF_RAW_INSN(BPF_JMP | BPF_CALL, 0, 0, 0, BPF_FUNC_map_lookup_elem),
BPF_JMP_IMM(BPF_JEQ, BPF_REG_0, 0, 2),
BPF_MOV64_IMM(BPF_REG_1, 1), /* r1 = 1 */
BPF_ATOMIC_OP(BPF_DW, BPF_ADD, BPF_REG_0, BPF_REG_1, 0),
BPF_MOV64_IMM(BPF_REG_0, 0), /* r0 = 0 */
BPF_EXIT_INSN(),
};

## Slide 14: bcc
BPF Compiler Collection
  Compiler framework and libraries for building BPF software
  https://github.com/iovisor/bcc
  Includes tracing , perf tools...
  Provides BPF front-ends:
      Python
      Lua
      C++
      C helper libraries
      golang(gobpf)

## Slide 15: bcc/BPF(C & Python)
bpf_text = """
#include <uapi/linux/ptrace.h>
#include <linux/blkdev.h>
struct proc_key_t {
char name[TASK_COMM_LEN];
u64 slot;
};
BPF_HISTOGRAM(dist, struct proc_key_t);
TRACEPOINT_PROBE(block, block_rq_issue)
{
struct proc_key_t key = {.slot = bpf_log2l(args->bytes / 1024)};
bpf_probe_read_kernel(&key.name, sizeof(key.name), args->comm);
dist.atomic_increment(key);
return 0;
}””
# load BPF program
b = BPF(text=bpf_text)
print("Tracing block I/O... Hit Ctrl-C to end.")
# trace until Ctrl-C
dist = b.get_table("dist")
try:
sleep(99999999)
except KeyboardInterrupt:
dist.print_log2_hist("Kbytes", "ProcessName", section_print_fn=bytes.decode)

## Slide 16: BPFtrace
Allow to to write ‘one liners’ or more simple BPF instruction
https://github.com/iovisor/bpftrace

## Slide 17: eXpress Data Path(XDP)
Allow to run eBPF on the network interface card instead of running on the CPU
Use kernel bypass technique
Avoid expensive context switches kSpace and uSpace
XDP program return action /verdict
    XDP_DROP, XDP_ABORTED
    XDP_PASS, XDP_TX
    XDP_REDIRECT
Example:
    attach_xdp()
https://github.com/xdp-project/xdp-paper/blob/master/xdp-the-express-data-path.pdf

## Slide 18: Demo

## Slide 21: Thanks
Mentor : Dr. Elana Copperman
LFX mentorship programs
Maintainers on mailing list